## Slide 1
Wanja Mössing
November 2018
Eyetracking Workshop
WS 18/19

## Slide 2
AlternativeTurorialbox
Today we will use 1 Eyetracker!
Create account at sr-support
Start

## Slide 3
Short: How does the Eyelink 1k+ work?
How to do gaze control in PTB & Psychopy?
Preparing EEG/ET coregistration in your experiment
Storing behavioral data in your eyetrack
Proper calibration
Converting .edf files: stupid (Matlab) & smart (R)
Preprocessing .edf files in R
Today

## Slide 4: How does the EL1000+ work?
Eyelink

## Slide 5
Huey (1908)

## Slide 6
Infrared based eyetracker
Infrared light is emitted to the eye
The lens records the eye from another angle
EL-host-PC detects pupil and Purkinje image
EL1k+

## Slide 7
Purkinje
pupil
Purkinje images

## Slide 8
Calibration
Cornea reflection = 1st purkinje image

## Slide 9
Calibration creates constellation-dependent coordinate system
Validation takes similar measurements and checks how much the screen position differs from the system‘s prediction
calibration

## Slide 10
When looking straight, subjects should look at top 25% of screen
Eye-to-monitor distance should be >=1.75*monitor width
Distance tracker<->Eye 40-70cm (ideally 50-55)
Tracker‘s top as close as possible to screens bottom
Tracker should be centered horizontally wrt screen
Illuminator: usually @75%
Check setup

## Slide 11
Usually, centering the tracked eye is best (use big knob)
Click on the tracked eye and make sure the eyelink thinks about it as „right“ or „left“
Tune lense manually
Click ‚a‘ for auto-threshold
Assure that pupil and CR are well filled and (best case) nothing else is highlighted in the same colors.
Try to improve things by manually adjusting thresholds with UP/DOWN and +/-
Have subject look in all corners of the screen and see if the above settings still look good
Good calibration

## Slide 12
Usually, centering the tracked eye is best (use big knob)
Click on the tracked eye and make sure the eyelink thinks about it as „right“ or „left“
Tune lense manually
Click ‚a‘ for auto-threshold
Assure that pupil and CR are well filled and (best case) nothing else is highlighted in the same colors.
Try to improve things by manually adjusting thresholds with UP/DOWN and +/-
Have subject look in all corners of the screen and see if the above settings still look good
Good calibration

## Slide 13
9-13 point calibration are most precise
Grid should be horizontally and vertically parallel (approx.)
  If not: redo setup
Cali-Vali

## Slide 14
Problem: Glasses reflect IR-light -> tracker thinks ist CR-reflection
Try this:
  Ask subject to move chin forward
  Adjust table height
  Move camera closer to subject (min distance: 40cm!)
  Lower position using big knob
  Adjust angle of camera
  Increase illumination
Glasses gone wild

## Slide 15
Two modes of tracking pupil
Ellipse interpolates parts of pupil that are occluded
Centroid uses center of mass
Centroid: Usually best, less noise
Ellipse: Good for people with low eyelids and tiny glasses
Ellipse vs Centroid

## Slide 16
Two modes of tracking pupil
Ellipse interpolates parts of pupil that are occluded
Centroid uses center of mass
Centroid: Usually best, less noise
Ellipse: Good for people with low eyelids and tiny glasses
Ellipse vs Centroid

## Slide 17
Usually happens when looking at top corners
Increase distance or lower threshold
CR smearing

## Slide 18: Software structure
Matlab / python
Experiments

## Slide 19
SR Developer‘s pack
Psychtoolbox comes with Eyelink toolbox
Psychopy comes with *too outdated* Eyelink module
  See my readme on github for how to update (don‘t use pip!)
My set of high-level Eyelink functions
  github.com/wanjam/wm_utilities/Eyelink
Install this (to record)

## Slide 20
SR Developer‘s pack
Matlab:
  Coregister EEG/ET: Olaf Dimigen‘s <EYE-EEG>
    Eeglab plugin manager is outdated. Use github: olafdimigen/eye-eeg
R:
  Parse edf files: Jason Hubbard‘s <edfr>
    devtools::install_github(‘jashubbard/edfr‘)
  Massage data: Hedderik van Rijn‘s <pR>, my <wmR>
    devtools::install_github(‘wanjam/wm_utilities/helper-funs/wmR‘)
    devtools::install_github(‘hedderik/pR‘)
Install this (to analyze)

## Slide 21
SR research provides a „developer‘s kit“
Newest version always in forum
Ubuntu: PPA (read instructions *very* careful)
Windows/Mac: zip/dmg
Core of everything (written in C++)  install!
Have a look: sr-support.com
SR-dev kit

## Slide 22
Software structure
SR’s developer’s kit

EDF datafiles

Gaze-control

Analysis

Stimulation PC

wm_utilities/Eyelink

Jason hubbard “edfr”

Psychtoolbox/Eyelink

## Slide 23: Functions for Experiments
Experiments

## Slide 24
wm_ utilities
Readme online! https://github.com/wanjam/wm_utilities/Eyelink

## Slide 25
wm_ utilities
I‘ll only talk about Matlab – Same functions for Python!

## Slide 26
wm_ utilities
I‘ll only talk about Matlab – Same functions for Python!

## Slide 27
[P, wPtr] = EyelinkStart(P, wPtr, “filename“)
 doc EyelinkStart
P = your structure with parameters
can be empty, can contain extra config stuff
Always back assign P!
Does this:
Starts and configures connection between EL and PC
Opens a file to write to
Defines sampling rate and what to store
Defines locations of calibration points
Nulls the TTL port
Runs an initial calibration
Connect

## Slide 28
EyelinkRecalibration(P)
Recalibrates the Eyetracker
Useful when:
Break
Subject moved a lot and eye is lost
Re-calibrate

## Slide 29
[didrecal, FixationOnset, hsmvd] = EyelinkControlFixation(P, Tmin, Tmax, loc, maxDegDeviation, eyelinkconnected, pixperdeg, dorecal, Igoreblinks)
Highest possible level in wm_utilities
Does this:
Takes a target location (loc)
Subject has <Tmax> seconds to look at the target
Subject has to look at target for <Tmin> seconds
If not: start a recalibration (If you want that)
Do you want to ignore blinks?
Control Fixation

## Slide 30
[x, y, hsmvd] = EyelinkGetGaze(P, Ignoreblinks, OverSamplingBehavior, targetXY, FixLenDeg, eyelinkconnected, pixperdeg)
Lower level: Just get the gaze position and check whether that differs from the last position.
Does this:
Checks if the Eyetracker has a new sample available
If so, return the (x, y) pixel coordinate pair of the current gaze
In addition, check if the current gaze differs more than <FixLenDeg> degree from targetXY. If so, <hsmvd> is true (1).
Get Gaze

## Slide 31
[message] = EyelinkSendTabMsg(varargin)
stores behavioral data coregistered with time and ttl into the .edf file
Does this:
Takes as many input arguments as you want
Converts everything to strings
Concatenates everything tab-delimited
Prepends a “<“
Sends <message> to .edf file
Behavioral data

## Slide 32
EyelinkStop(P, eyelinkconnected)
Finishes recording and puts Eyelink to standby
Does this:
Stops the recording
Copies the final file from the EL-host PC to the stimulation PC
Then puts the Eyelink to standby
Stop recording

## Slide 33
EyelinkNotify(message, eyelinkconnected)
Lower level: Just get the gaze position and check whether that differs from the last position.
Does this:
Checks if the Eyetracker has a new sample available
If so, return the (x, y) pixel coordinate pair of the current gaze
In addition, check if the current gaze differs more than <FixLenDeg> degree from targetXY. If so, <hsmvd> is true (1).
Status Notifier

## Slide 34
EyelinkNotify(message, eyelinkconnected)
Lower level: Just get the gaze position and check whether that differs from the last position.
Does this:
Checks if the Eyetracker has a new sample available
If so, return the (x, y) pixel coordinate pair of the current gaze
In addition, check if the current gaze differs more than <FixLenDeg> degree from targetXY. If so, <hsmvd> is true (1).
Status Notifier

## Slide 35
EyelinkAvoidWrongTriggers
Prevents EEG-trigger-mess
Should be at the top of your non-eyetracking experiment
Does this:
Checks if the Eyelink-host pc is turned on
Throws an error if that‘s the case
TTL trigger

## Slide 36
‚eyelinkconnected‘ = boolean – if false, all functions are dummies
Dummymode doesn‘t always work for me, but it‘s worth trying
Para-meters

## Slide 37: Implement Gazecontrol
DIY

## Slide 38
Open a terminal and run >ptb3-matlab
Go to /home/tutorialbox/Documents/MATLAB/Tutorial/Task
Start the experiment once by running >TutorialExperiment.m
DIY

## Slide 39
Add code to start and stop the Eyelink
Display „Ruebezahl“ as status message, right after EyelinkStart
Display the current trial number as status message
Recalibrate after each break.
Control that subjects look at the fixation symbol.
Send „triggers“ (i.e., messages) after all relevant flips.
Store the resulting behavioral data in the .edf
If time: try to make the target‘s position gaze-dependent
DIY

## Slide 40: Preprocessing
Analyze

## Slide 41
Coregistration with EEG data:
  Fixation Related Potentials  follow EYE-EEG/Elektro-Pipe
Pupil Dilation
Saccades
Fixations
Gazepaths
…
 Most stuff possible after following this template…
What‘s possible?

## Slide 42
edf2asc: binary available in the terminal (from the devpack)
EYE-EEG
  parseyelink(file.asc)  converts .asc to .mat
  pop_importeyetracker(EEG, file.asc)  coregistration
Elektro-Pipe
  func_importEye combines all three and plots quality
  Called by prep01_preproc
Parse
Matlab

## Slide 43
Jason Hubbard‘s edfr uses the devpack‘s C++ code directly
  No need for edf2asc
  Most sophisticated package for parsing (afaik)
  edf.all(), edf.recordings(), edf.events()
  = ET-data, Header, TTL
Parse R

## Slide 44
Open Rstudio in the VirtualBox
You‘ll find a file called tutorial_preprocEDF.R
Let‘s first walk through that…
Challenge:
  Set the output time vector relative to fixation onset
  Go to line 213. Try to add more info (as added in the experiment)
  Add the new info to all necessary lines.
DIY